## Slide 1: Digital Communication 21EC51

## Slide 2: Module 1 Digital Modulation Techniques:

## Slide 3: Module 1
Digital Modulation Techniques: Phase shift Keying techniques using coherent detection: generation, detection and error probabilities of BPSK and QPSK, M–ary PSK, M–ary QAMFrequency shift keying techniques using Coherent detection: BFSK generation, detection and error probability.
Non coherent orthogonal modulation techniques: : BFSK, DPSK Symbol representation, Block
diagrams treatment of Transmitter and Receiver, Probability of error (without derivation of probability of error equation)

## Slide 4: Introduction
Digital baseband transmission where the generated data stream, represented in the form of discrete pulse-amplitude modulated signal (PAM) is transmitted directly over a low-pass channel.
Digital pass-band transmission where the incoming digital signal is modulated onto a carrier (usually sinusoidal) with fixed frequency limits imposed by the bandpass channel available
The communication channel used in pass-band digital transmission may be microwave radio link, satellite channel etc.

## Slide 5: Introduction
Definitions:
The modulation of digital signals is a process involving switching (keying) the amplitude, frequency or phase of a sinusoidal carrier in some way in accordance with the incoming digital data.
Three basic schemes exist:
Amplitude Shift Keying (ASK)
Frequency Shift Keying (FSK)
Phase Shift Keying (PSK)

## Slide 6: Introduction
REMARKS:
In continuous wave modulation phase modulated and frequency modulated signals are difficult to distinguish between, this is not true for PSK and FSK.
PSK and FSK both have constant envelope while ASK does not.
Figure : Illustrative waveforms for the three basic forms of signaling binary information.
Amplitude-shift keying. (b) Phase-shift keying.(c) Frequency-shift keying

## Slide 7: Module 2
By definition of the AWGN model it has zero mean
The PDF of correlator is given by

## Slide 8: Binary Phase Shift Keying (BPSK)
In BPSK ,phase of sinusoidal carrier is changed according in to the data bit transmitted.
In a binary PSK system, the pair of fixed amplitude and frequency signals and used to represent binary symbols 1 and 0,except that carrier phase of each symbol differs by phase of .
For Symbol 1
For Symbol 0
A pair of sinusoidal waves that differ only in a relative phase-shift of 180°, are defined in the above equations, is referred to as an antipodal signal.

## Slide 9: Signal-Space Diagram of Binary PSK Signals
From this pair of equations or antipodal signal, In BPSK there is only one basis function of unit energy expressed as:
A coherent BPSK system can be characterized by having a signal space that is one dimensional (N= 1), with signal constellation consisting of two message points (M = 2)
So the transmitted signals can be expressed as:
The coordinates of the message points are

## Slide 10: Signal-Space Diagram of Binary PSK Signals
The coordinates of the message points are
Figure:
(a). Signal-space diagram for coherent binary PSK system. (b). The waveforms depicting the transmitted signals s1 (t) and s2 (t), displayed in the inserts, assume = 2
Note : That the frequency is chosen to ensure that each transmitted bit contains an integer number of cycles.
is an integer such that

## Slide 11: Generation and Detection of Coherent BPSK Signals
Transmitter side: consists of two components:
Polar NRZ-level encoder, which represents symbols 1 and 0 of the incoming binary sequence by amplitude levels and , respectively.
Product modulator, which multiplies the output of the polar NRZ encoder by the basis function ;in effect, the sinusoidal .
acts as the “carrier” of the binary PSK signal
Carrier wave is with frequency fc=(nc /Tb )
Figure: Block diagrams of binary PSK transmitter.
For Symbol 1
For Symbol 0
WKT

## Slide 12: Generation and Detection of Coherent BPSK Signals
Receiver side:
Noisy PSK is fed to a correlator with locally generated reference signal.
Correlator, which correlates the received signal x(t) with the basis function on a bit-by-bit basis.
Decision device, which compares the correlator output against a zero-threshold, assuming that binary symbols 1 and 0 are equiprobable. If the threshold is exceeded, a decision is made in favor of symbol 1; if not, the decision is made in favor of symbol 0.
Figure: Block diagrams of binary PSK Receiver

## Slide 13: Error Probability of Binary PSK
Decision rule: based on the maximum likelihood decision algorithm/rule which in this case means that we have to choose the message point closest to the received signal point.
For BPSK: N= 1, space is divided into two areas (Figure.)
The set of points closest to message point 1 at
The set of points closest to message point 2 at
The decision rule is simply to decide that signal (i.e. binary 1) was transmitted if the received signal point falls in region , and decide that signal (i.e. binary symbol 0) was transmitted if the received signal falls in region .
Figure: Signal-space diagram for coherent binary PSK system.

## Slide 14: Error Probability of Binary PSK
Two kinds of errors are possible due to noise:
Error of the first kindis transmitted but the noise is such that the received signal point falls inside region ; so the receiver decides in favor of signal .
Error of the second kind: Signal is transmitted but the noise is such that the received signal point falls inside region ; so the receiver decides in favor of signal
To calculate the probability of making an error of the first kind, we note from Figure that the decision region associated with symbol 1 or signal is described by
The observed element is expressed as a function of
The received signal x(t) as:
Figure: Signal-space diagram for coherent binary PSK system.

## Slide 15: Error Probability of Binary PSK
The observed element is expressed as a function of the received signal x(t) as:
Let x(t) be the received signal
Let us assume symbol ‘0’ is transmitted the correlator output is given by
Figure: Signal-space diagram for coherent binary PSK system.

## Slide 16: Error Probability of Binary PSK
Where is random variable of additive Gaussian noise having zero mean and variance mean of the random variable is
Variance of the random variable is
since the variance of constant is zero

## Slide 17: Error Probability of Binary PSK
The conditional probability density function of random variable X1, given that symbol 0 (i.e., signal s2(t)) was transmitted, is given by

## Slide 18: Error Probability of Binary PSK
Let denotes the conditional probability of the receiver deciding in favor of symbol 1, when symbol 0 was transmitted, is therefore

## Slide 19: Error Probability of Binary PSK
WKT the complementary error function is given by
Using equation 2 the equation 1 can be written as
Similarly

## Slide 20: Error Probability of Binary PSK
Let the probability of transmitting symbol ‘0’ is =
Let the probability of transmitting symbol ‘1’ is =
The average probability error
=+
So increasing the signal energy per bit makes the points and move farther apart which correspond to reducing the error probability

## Slide 21: Coherent Phase Shift Keying - QPSK
Bandwidth-conserving modulation scheme known as QuadriPhase-Shift Keying (QPSK)
Reliable performance
Very low probability of error
Efficient utilization of channel bandwidth
Sending more then one bit in a symbol

## Slide 22: Coherent Phase Shift Keying - QPSK
Quadriphase-shift keying (QPSK) Example of quadrature carrier multiplexing
Information is carried in the phase
Phase can take one of four equally spaced values – π/4, 3π/4, 5π/4, 7π/4
Transmitted signal is defined as:
where E is the transmitted signal energy per symbol and T is the symbol duration.
Each possible value of the phase corresponds to a unique dibit (i.e., pair of bits).
A set of phase values are used to represent the Gray-encoded set of dibits, 10, 00, 01, and 11, where only a single bit is changed from one dibit to the next.

## Slide 23: Coherent Phase Shift Keying - QPSK
Signal-Space Diagram of QPSK Signals:
Using a well-known trigonometric identity, we may expand the above equation to redefine the transmitted signal in the canonical form:
where i = 1, 2, 3, 4. Based on this representation, we make two observations

## Slide 24: Coherent Phase Shift Keying - QPSK
Signal-Space Diagram of QPSK Signals:
where i = 1, 2, 3, 4.
There are two orthonormal basis functions, defined by a pair of quadrature carriers:
Based on this representation, we make two observations

## Slide 25: Coherent Phase Shift Keying - QPSK
Signal-Space Diagram of QPSK Signals:

## Slide 26: Coherent Phase Shift Keying - QPSK

## Slide 27: Coherent Phase Shift Keying - QPSK
Signal-Space Diagram of QPSK Signals:
Accordingly, a QPSK signal has a two-dimensional signal constellation (i.e., N = 2) and four message points (i.e., M = 4) whose phase angles increase in a counterclockwise direction, as illustrated in Figure .
Figure : Signal-space diagram of QPSK system
Elements of the signal vectors, namely si1 and si2, have their values summarized in Table; the first two columns give the associated dibit and phase of the QPSK signal.

## Slide 28: Generation and Detection of QPSK Signals
The two orthonormal basis functions, defined by a pair of quadrature carriers:
As an example consider the case i=1 or dibit 01 and nothing that E = 2
Figure : Block diagram of QPSK transmitter

## Slide 29: Generation and Detection of QPSK Signals
Transmitter:
Input binary data sequence transformed into polar form (nonreturn-to-zero encoder).
Symbols 1 and 0 are represented by +√E/2 and -√E/2The two orthonormal basis functions, defined by a pair of quadrature carriers.
Divided into two streams by a demultiplexer (odd and even numbered bits) a1 (t) and a2 (t)
In any signaling interval the amplitudes of a1 (t) and a2 (t) equal si1 and si2 depending on the particular bit that is sent.
a1 (t) and a2 (t) modulate a pair of quadrature carriers (orthogonal basis functions φ1 (t) = √2/Tcos(2πfc t) and φ2 (t)= √2/Tsin(2πfc t) )
Figure : Block diagram of QPSK transmitter
The QPSK transmitter may be viewed as two binary PSK generators that work in parallel, each at a bit rate equal to one-half the bit rate of the original binary sequence at the QPSK transmitter input

## Slide 30: Generation and Detection of QPSK Signals
Receiver:
Pair of correlators, which have a common input x(t). The two correlators are supplied with a pair of locally generated orthonormal basis functions and which means that the receiver is synchronized with the transmitter. The correlator outputs, produced in response to the received signal x(t), are denoted by x1 and x2, respectively.
Pair of decision devices, which act on the correlator outputs x1 and x2 by comparing each one with a zero-threshold; here, it is assumed that the symbols 1 and 0 in the original binary stream at the transmitter input are equally likely. If x1 > 0, a decision is made in favor of symbol 1 for the in-phase channel output; on the other hand, if x1<0, then a decision is made in favor of symbol 0. Similar binary decisions are made for the quadrature channel.
Figure : Block diagram of coherent QPSK receiver.
Multiplexer, the function of which is to combine the two binary sequences produced by the pair of decision devices. The resulting binary sequence so produced provides an estimate of the original binary stream at the transmitter input.

## Slide 32: Error Probability of QPSK
The received signal x(t) is defined as
The observed element is the two correlator outputs,
x1 and x2, are respectively defined as follows:
Consider transmission of symbol then the output of top correlator and bottom correlotor is given by
Thus, the observable elements x1 and x2 are sample values of independent Gaussian random variables with mean values equal to and , respectively, and with a common variance equal to N0/2

## Slide 33: Error Probability of QPSK
When the symbol is transmitted, the received signal point lies in the decision region the conditional probability is given by

## Slide 34: Error Probability of QPSK
When the symbol is transmitted, the received signal point lies in the decision region ,then and .
The probability of correct decision is equal to the probability of joint event > 0 and > 0 .
Since the two events are independent we can write the probability of correct decision

## Slide 36: Error Probability of QPSK

## Slide 37: Error Probability of QPSK

## Slide 38: Error Probability of QPSK

## Slide 39: Error Probability of QPSK
Thus the average probability for a symbol error for coherent QPSK can be written as:
The term (√E/2N0 )<< 1 so it can be ignored, then:
Since there are two bits per symbol in the QPSK system, the energy per symbol is related to the energy per bit in the following way:

## Slide 40: BPSK
Signal Expressed in terms of Basis Function
Coherent BPSK

## Slide 41: QPSK
Each possible value of phase corresponds to symbol represented by unique pair of bits called dibits
Coherent QPSK

## Slide 42: M-ary PSK
More general case than QPSK
Phase carrier takes one of M possible values, θi= 2(i-1)π/M, where i = 1,2,…M-1
During each signaling interval of duration T the M-ary PSK waveform is given by

## Slide 43: M-ary PSK
si(t) can be expanded using the basis φ1(t) and φ2(t)
Thus we may express the transmitted signal si(t) in terms of basis function as follows:

## Slide 44: M-ary PSK :signal constellation Diagram
The Figure shows a constellation diagram for octaphase-shift-keying (i.e., M = 8).
The signal constellation is two dimensional.
The M message points are equally spaced on a circle of radius and centered at the origin.
The decision boundary is shown by dashed lines.
Figure :(a) Signal-space diagram for octaphase-shift keying (i.e., M  8). The decision boundaries are shown as dashed lines.

## Slide 45: Error Probability of M-ary PSK:
Figure :(a) Signal-space diagram for octaphase-shift keying (i.e., M  8). The decision boundaries are shown as dashed lines. (b) Signal-space diagram illustrating the application of the union bound for octaphase-shift keying.

## Slide 46: Error Probability of M-ary PSK:
The signal constellation is two dimensional.
The M message points are equally spaced on a circle.
Suppose that the transmitted signal corresponds to the message point ,whose coordinates along the and are and 0 respectively.
Suppose that the ratio is large enough to consider the nearest two message points, one on either side of ,as potential candidate for being mistaken for due to channel noise.
The Euclidian distance between each two points form is for M = 8 can be calculated as:

## Slide 47: M-ary PSK:

## Slide 48: Power spectra of M-ary PSK Signals
Symbol duration for M-ary PSK is defined as:
The baseband power spectral density of M-ary PSK is given by:

## Slide 49: Power spectra of M-ary PSK Signals
Figure :Power spectra of M-ary PSK signals for M  2, 4, 8.

## Slide 50: Bandwidth Efficiency of M-ary PSK Signals
From the previous slide of the power spectra of the M-ary PSK it is visible that we have a well defined main lobe and spectral nulls.
Main lobe provides a simple measure for the bandwidth of the M-ary PSK. (null-to-null bandwidth).
The channel bandwidth is given by:

## Slide 51: Bandwidth Efficiency of M-ary PSK Signals
Also, we have from before
So we can express the bandwidth in terms of bit rate as:
Is the bit rate expressed as bits per second.

## Slide 52: Bandwidth Efficiency of M-ary PSK Signals
The bandwidth efficiency of M-ary PSK signals is given by
As the number of states in M-ary PSK is increased, the bandwidth efficiency is improved at the expense of error performance
Table : Bandwidth efficiency of M-ary PSK signals

## Slide 53: M-ary Quadrature Amplitude Modulation
In M-ary Quadrature Amplitude Modulation In an M-ary PSK system, the in-phase and quadrature components of the modulated signal are interrelated in such a way that the envelope is constrained to remain constant.
if this constraint is removed so as to permit the in-phase and quadrature components to be independent, we get a new modulation scheme called M-ary QAM. The QAM is a hybrid form of modulation.

## Slide 54: M-ary Quadrature Amplitude Modulation
The transmitted M-ary QAM signal for symbol k can now be defined in terms of E0:
The signal sk(t) involves two phase-quadrature carriers, each one of which is modulated by a set of discrete amplitudes; hence the terminology “quadrature amplitude modulation.”
In M-ary PAM, the signal-space diagram is one-dimensional. M-ary QAM is a two-dimensional generalization of M-ary PAM, in that its formulation involves two orthogonal passband basis functions:

## Slide 55: M-ary Quadrature Amplitude Modulation
QAM Square Constellations:
A QAM square constellation can be factored into the product of the corresponding L-ary PAM constellation with itself.
In Figure we have constructed two signal constellations for the 4-ary PAM, one vertically oriented along the 1-axis in part of the figure, and the other horizontally oriented along the 2-axis in part b of the figure. These two parts are spatially orthogonal to each other
Figure: The two orthogonal constellations of the 4-ary PAM.
(a) vertically oriented constellation.
(b) Horizontally oriented constellation. As mentioned in the text, we move top-down along the 2-axis and from left to right along the 1-axis

## Slide 56: M-ary Quadrature Amplitude Modulation
QAM Square Constellations:
In developing two dimensional structure, the following points should be remembered:
The same binary sequence is used for both 4-ary PAM constellations.
The Gray encoding rule is applied, which means that as we move from one codeword to an adjacent one, only a single bit is changed.
In constructing the 4-ary QAM constellation, we move from one quadrant to the next in a counterclockwise direction. With four quadrants constituting the 4-ary QAM.
Figure: The two orthogonal constellations of the 4-ary PAM.
(a) vertically oriented constellation.
(b) Horizontally oriented constellation. As mentioned in the text, we move top-down along the 2-axis and from left to right along the 1-axis

## Slide 57: M-ary Quadrature Amplitude Modulation
QAM Square Constellations:
Stage 1: First-quadrant constellation. Referring to Figure , we use the code words along the positive parts of the 2 and 1-axes, respectively, to write
Stage 2: Second-quadrant constellation. Following the same procedure as in Stage 1, we write
Figure: The two orthogonal constellations of the 4-ary PAM.
(a) vertically oriented constellation.
(b) Horizontally oriented constellation. As mentioned in the text, we move top-down along the 2-axis and from left to right along the 1-axis

## Slide 58: M-ary Quadrature Amplitude Modulation
QAM Square Constellations:
Stage 3: Third-quadrant constellation. Again, following the same procedure as before, we next write
Stage 4: Fourth-quadrant constellation. Finally, we write
Figure: The two orthogonal constellations of the 4-ary PAM.
(a) vertically oriented constellation.
(b) Horizontally oriented constellation. As mentioned in the text, we move top-down along the 2-axis and from left to right along the 1-axis

## Slide 59: M-ary Quadrature Amplitude Modulation
QAM Square Constellations:
The final step is to piece together these four constituent 4-ary PAM constellations to construct the 4-ary QAM constellations as described in Figure .
The important point to note here is that all the codewords in Figure obey the Gray encoding rule, not only within each quadrant but also as we move from one quadrant to the next
Figure :(a) Signal-space diagram of M-ary QAM for M = 16; the message points in each quadrant are identified with Gray-encoded quadbits.

## Slide 60: M-ary Quadrature Amplitude Modulation
Average Probability of Error
The average probability of error of the M-ary QAM by proceeding as
1.The probability of correct detection for M-ary QAM is written as
Where Pe’ is the probability of symbol error for the L-ary PAM
2.With ,L=√M the probability of symbol error Pe’ is itself defined by
3.The probability of symbol error for M-ary QAM is given by
Hence, using above equations, we find that the probability of symbol error for M-ary QAM is approximately given by
The transmitted energy in M-ary QAM is variable, in that its instantaneous value naturally depends on the particular symbol transmitted. Therefore, it is more logical to express Pe in terms of the average value of the transmitted energy rather than E0 .
For M=4, in the above equation E av = E, where E is the energy per symbol, we find that the resulting formula for the probability of symbol error becomes identical to that in QPSK.

## Slide 61: Frequency-Shift Keying Techniques Using Coherent Detection
Binary FSK
A nonlinear method of modulation known as FSK using coherent detection.
In binary FSK, symbols 1 and 0 are distinguished from each other by transmitting one of two sinusoidal waves that differ in frequency by a fixed amount.
A typical pair of sinusoidal waves is described by

## Slide 62: Frequency-Shift Keying Techniques Using Coherent Detection
Binary FSK
A typical FSK waveform is described by
Where i = 1, 2 and Eb is the transmitted signal energy per bit;
The transmitted frequency is given by
Where n c is some fixed integer and i=1, 2.

## Slide 63: Frequency-Shift Keying Techniques Using Coherent Detection
Binary FSK
The two orthonormal basis functions are given by
Thus the FSK signal s I (t) can be expressed in terms of basis functions as follows

## Slide 64: Frequency-Shift Keying Techniques Using Coherent Detection
Binary FSK
Thus the two signals are represented in the vector form as follows:

## Slide 65: Frequency-Shift Keying Techniques Using Coherent Detection
Binary FSK
Thus the two signals are represented in the vector form as follows:
Figure : Signal-space diagram for binary FSK system.

## Slide 66: BFSK: Decision Rule
Let x(t) be the received signal and is defined
Given that symbol 1 was transmitted, x(t) equals s1(t) + w(t), where w(t) is the sample function of a white Gaussian noise process of zero mean and power spectral density N02. If, on the other hand, symbol 0 was transmitted, x(t) equals s2(t) + w(t).
The observation vector x has two elements x1 and x2 that are defined by, respectively,
Figure : Signal-space diagram for binary FSK system.

## Slide 67: BFSK: Decision Rule
The signal space is partitioned into two regions
The receiver decides in favor of symbol 1 if the received signal point represented by the observation vector x falls inside region Z1. This occurs when x1  x2, or (x1 - x2 ) > 0.
The receiver decides in favor of symbol 0 if the received signal point represented by the observation vector x falls inside region Z1. This occurs when x1 < x2, or (x1 - x2 ) < 0.
On the decision boundary, we have x1 = x2, in which case the receiver makes a random guess in favor of symbol 1 or 0.
Figure : Signal-space diagram for binary FSK system.

## Slide 68: Error Probability of Binary FSK
Let us define a new Gaussian random variable L whose sample value l is equal to the difference between x1 and x2; Thus l = x1 - x2
Given the symbol 1 or s1(t) was transmitted ,we have
Given the symbol 0 or s2(t) was transmitted ,we have

## Slide 69: Error Probability of Binary FSK
The variance of the random variable L is independent of which binary symbol was sent. Since the random variables X1 and X2 are statistically independent, each with a variance equal to N02, it follows that
Var [L]=Var [X1 ]+ Var [X2 ]= N0
We can recall that given a random variable X with µ and as the mean and variance , The conditional probability density function is given by
Suppose we know that symbol 0 is transmitted , The conditional probability density function of the random variable L equals

## Slide 70: Error Probability of Binary FSK
Due to noise ,the received signal point X falls inside the region Z1.So the receiver decides in favor of symbol 1. In Z1we have x1  x2, or (x1 - x2 ) > 0. Hence l > 0.
The conditional probability of error given that symbol 0 was transmitted is given by

## Slide 71: Error Probability of Binary FSK

## Slide 72: Error Probability of Binary FSK
WKT the complementary error function is given by

## Slide 73: Error Probability of Binary FSK
Similarly
Let the probability of transmitting symbol ‘0’ is =
Let the probability of transmitting symbol ‘1’ is =
The average probability error
=+

## Slide 74: BFSK transmitter
>

## Slide 75: BFSK transmitter
It consists of two components:
1. On–off level encoder: the output of which is a constant amplitude of in response to input symbol 1 and zero in response to input symbol 0.
2. Pair of oscillators: whose frequencies f1 and f2 differ by an integer multiple of the bit rate 1Tb. The lower oscillator with frequency f2 is preceded by an inverter.
When in a signaling interval, the input symbol is 1, the upper oscillator with frequency f1 is switched on and signal s1(t) is transmitted, while the lower oscillator is switched off.
On the other hand, when the input symbol is 0, the upper oscillator is switched off, while the lower oscillator is switched on and signal s2(t) with frequency f2 is transmitted.
Figure : Block diagram for binary FSK transmitter

## Slide 76: BFSK receiver.
To coherently detect the original binary sequence given the noisy received signal x(t), we may use the receiver shown in Figure.
It consists of two correlators with a common input, which are supplied with locally generated coherent reference signals 1(t) and 2(t).
The correlator outputs are then subtracted, one from the other; the resulting difference l is then compared with a threshold of zero. If l  0, the receiver decides in favor of 1.
On the other hand, if l  0, it decides in favor of 0.
If l is exactly zero, the receiver makes a random guess (i.e., flip of a fair coin) in favor of 1 or 0.
Figure : Block diagram for binary FSK receiver.

## Slide 77: Non-coherent Orthogonal Modulation Techniques
Coherent systems need carrier phase information at the receiver and they use matched filters to detect and decide what data was sent , while noncoherent systems do not need carrier phase information and use methods like square law to recover the data.
In noncoherent systems, the structure of the receiver is simple compared to coherent systems. Under large signal to noise ratios ,the performances of non coherent receivers approach that of coherent receivers.

## Slide 78: Non-coherent Orthogonal Modulation Techniques
Consider a binary signaling scheme that involves the use of two orthogonal signals s1 (t) and s2 (t), which have equal energy. Let the signaling interval 0  t  T.
Let these two signals is sent over an imperfect channel that shifts the carrier phase by an unknown amount.
Let g1 (t) and g2 (t) denote the phase-shifted versions of s1(t) and s2(t) that result from this transmission, respectively.
It is assumed that the signals g1(t) and g2 (t) remain orthogonal and have the same energy E, regardless of the unknown carrier phase. We refer to such a signaling scheme as non-coherent orthogonal modulation.
In addition to carrier-phase uncertainty, the channel also introduces AWGN w (t) of zero mean and power spectral density N0 2, resulting in the received signal.

## Slide 79: Binary Frequency-Shift Keying Using Noncoherent Detection
For the noncoherent detection of this frequency-modulated signal, the receiver consists of a pair of matched filters followed by envelope detectors, as in Figure.
The filter in the upper path of the receiver is matched to cos(2f1t) and the filter in the lower path is matched to cos(2f2t) for the signaling interval 0  t  Tb.
The resulting envelope detector outputs are sampled at t = Tb and their values are compared. The envelope samples of the upper and lower paths in Figure are shown as l1 and l2.
The receiver decides in favor of symbol 1 if l1 > l2 and in favor of symbol 0 if l1  l2. If l1 = l2, the receiver simply guesses randomly in favor of symbol 1 or 0.
Probability of error for Non coherent BFSK is
Figure : Noncoherent receiver for the detection of binary FSK signals.

## Slide 80: Differential Phase-Shift Keying (DPSK)
The DPSK is the “noncoherent” version of BPSK. The transmitter involves two operations:
  Differential encoding of the input binary sequence and
  PSK of the encoded sequence,.
The differential encoded sequence d k is generated by the logical equation
Differential encoding starts with an arbitrary first bit, serving as the reference bit; to this end, symbol 1 is used as the reference bit.
Generation of the differentially encoded sequence then proceeds in accordance with a two-part encoding rule as follows:
1. If the new bit at the transmitter input is 1, leave the differentially encoded symbol unchanged with respect to the current bit.
2. If, on the other hand, the input bit is 0, change the differentially encoded symbol with respect to the current bit.

## Slide 81: Binary Phase Shift Keying (BPSK)
In BPSK ,phase of sinusoidal carrier is changed according in to the data bit transmitted.
In a binary PSK system, the pair of fixed amplitude and frequency signals and used to represent binary symbols 1 and 0,except that carrier phase of each symbol differs by phase of .
For Symbol 1
For Symbol 0
A pair of sinusoidal waves that differ only in a relative phase-shift of 180°, are defined in the above equations, is referred to as an antipodal signal.

## Slide 82: Differential Phase-Shift Keying
The differentially encoded sequence, denoted by {d k}, is used to shift the sinusoidal
Carrier phase by zero and 180o, representing symbols 1 and 0, respectively. Thus, in terms of phase-shifts, the resulting DPSK signal follows the two-part rule:
1. To send symbol 1, the phase of the DPSK signal remains unchanged.
2. To send symbol 0, the phase of the DPSK signal is shifted by 180°
Table :Illustrating the generation of DPSK signal

## Slide 83: Differential Phase-Shift Keying
Table :Illustrating the generation of DPSK signal

## Slide 84: Error Probability of DPSK
DPSK Signal during symbol 1 transmission
Suppose the transmitted DPSK signal equals for duration 0  t  Tb.
Let s1(t)the transmitted DPSK signal for 0  t  Tb, for the case when we have binary symbol 1 at the transmitter input for the second-bit interval Tb  t  2Tb. The transmission of 1 leaves the carrier phase unchanged.

## Slide 85: Error Probability of DPSK
DPSK Signal during symbol 0 transmission
Suppose the transmitted DPSK signal equals for duration 0  t  Tb.
Let s2(t)the transmitted DPSK signal for 0  t  Tb, for the case when we have binary symbol 0 at the transmitter input for the second-bit interval Tb  t  2Tb. The transmission of 0 leaves the carrier phase advanced by 180 degrees.

## Slide 86: Error Probability of DPSK
For DPSK, we have T = 2Tb and E = 2Eb. Hence, average Probability of Error for non-coherent DPSK is given by

## Slide 87: Generation of DPSK Signal
Figure shows the block diagram of the DPSK transmitter . To be specific, the transmitter consists of two functional blocks:
• Logic network and one-bit delay (storage) element, which are interconnected so as
to convert the raw input binary sequence {bk} into the differentially encoded sequence {dk}.
• Binary PSK modulator, the output of which is the desired DPSK signal.
Figure : Block diagram of a DPSK transmitter.

## Slide 88: Optimum Receiver for the Detection of DPSK
Case 1:
Case 2:

## Slide 89: Optimum Receiver for the Detection of DPSK
Figure : Signal-space diagram of received DPSK signal
We have Signal-space diagram where the received signal points over the two bit interval are by (Acos, Asin) and (–Acos, –Asin), where A denotes the carrier amplitude.
Case 1:
Case 2:

## Slide 90: Optimum Receiver for the Detection of DPSK
The receiver measures the coordinates (xi0, xq0 ), first, at time t = Tb and ((xi1, xq1 ) then measures at time t = 2Tb.
The issue to be resolved is whether these two points map to the same signal point or different ones.
The signal points (xi0, xq0 ), and (xi1, xq1 ) are represented by the vectors x0, and x1 .
If the transmitted symbol is 1 then the two vectors lies roughly in the same direction. Then their inner product is positive.

## Slide 91: Optimum Receiver for the Detection of DPSK
If the transmitted symbol is 0 then the two vectors lies roughly in the opposite direction. Then their inner product is negative.
Accordingly we may write

## Slide 92: Optimum Receiver for the Detection of DPSK
The optimum receiver for the detection of binary DPSK is as shown in Figure. The receiver of Figure is said to be optimum for two reasons:
In structural terms, the receiver avoids the use of fancy delay lines that could be needed otherwise.
In operational terms, the receiver makes the decoding analysis straightforward to handle, in that the two signals to be considered are orthogonal over the interval [0,2Tb].
Figure : Block diagram of a DPSK Receiver

## Slide 93: Formulas

## Slide 94: Problem 3.1

## Slide 95: Problem 3.1

## Slide 96: Problem 3.1

## Slide 97: Problem 3.2

## Slide 98: Problem 3.2

## Slide 99: Problem 3.2

## Slide 100: Formulas

## Slide 101: Problem 3.3

## Slide 102: Problem 3.3

## Slide 103: Problem 3.3

## Slide 104: Problem 3.3

## Slide 105: Problem 3.4

## Slide 106: Problem 3.4

## Slide 107: Problem 3.4

## Slide 108: Problem 3.5
Q 3.5. Sketch the in phase and quadrature components of a QPSK signal for the binary sequence 1 1 0 0 1 0 1 1 1
Solution: Let us choose basis function for QPSK as and
Given
{bi } = {1 1 0 0 1 0 1 1 1}
{b ei } = {1 0 1 1 1}
{b oi } = {1 0 0 1 }

## Slide 109: Problem 3.5
Solution: Let us choose basis function for QPSK as and
Given
{bi } = {1 1 0 0 1 0 1 1 1}
{b oi } = {1 0 0 1 }

## Slide 110: Problem 3.6
Q 3.6:A binary sequence 1 0 1 1 0 1 is transmitted over communication channel using DPSK transmitter (a) Sketch the transmitted DPSK waveform assuming an initial bit of 1.(b) Assuming the channel is noise free, show that the DPSK detector produces the original binary sequence.
Solution: the logic used for generating DPSK sequence {dk} is given by

## Slide 111: Problem 3.6
(b)

## Slide 112: Problem 3.7
Q 3.7:generate BPSK and DPSK waveforms for a given binary sequence 11 0 1 11 0 1 is transmitted over communication channel.
Solution: The logic used for generating BPSK
sequence

## Slide 113: Problem 3.7

## Slide 114: Problem 3.7

## Slide 115: Problem 3.8
Q 3.8:the input binary sequence to a qpsk modulator is 0 1 0 0 1 0 1 1 0 1 1 sketch the transmitted carrier as a function of time.
Solution: The transmitted phase for each dibit as follows

## Slide 116: Problem 3.8

## Slide 117: , )
(
(
X(t)
X(t)
.
(t)

## Slide 118: Error Probability of Binary PSK
The conditional probability density function that xj (signal sj was received providing mi was sent) is given by:
The conditional probability density function of random variable X1, given that symbol 0 (i.e., signal s2(t)) was transmitted, is defined by
Substituting the value in the above equation

## Slide 120: , )
π
(
(
X(t)
X(t)
.
(t)

## Slide 121: x(t)=
x(t)=

## Slide 122: , )
(
(
X(t)
X(t)
.

## Slide 123
j (t)
j (f)
= sgn(f)]
+ = [j (t)] +[j (t)]
+ =2
x(t) =